Observational Project: Photometry
AST 3Y03
Ian Fare – 001413393
January 30, 2017

Quantities needed for each image
Quantity IRAF name	How to find	Value image 1	Value image 2
Full Width Half fwhmpsf in datapars Max (pixels)	imexamine 'r'	3.808	3.659
Read Noise readnoi in datapars (electrons)	FITS header	3.725	3.725
Gain (electrons epadu in datapars per count)	FITS header	2.425	2.425
Min good data datamin in datapars value (counts)	-3*read noise in counts	8.175	8.175
Max good data datamax in datapars value (counts)		32000	32000
Standard deviation sigma in datapars of background in counts	√(s + r2 ) s = sky value from imexamine 'h'; r=read noise in electrons	17.26675	110.648726
Centroid algorithm calgori in centerpars		centroid	centroid
Size of centroid box (pixels) cbox in centerpars	2*FWHM	7.616	7.318
Inner radius of sky annulus in fitskypars annulus (pixels)	Aperture + 5 pixels	20.232	19.646
Width of sky annulus (pixels) dannulu in fitskypars	5 – 10	5	5
Size of aperture (pixels) apertur in photpars	4*FWHM	15.232	14.636

Description of procedures
For the most part, to perform photometry I followed the instructions given, and they worked pretty well. To summarize, for the first image, obj720.fits I did the following:
1. Found the required quantities by looking in the image’s FITS header and using imexamine as instructed.
2. Used epar phot to input these parameters for use by the daofind and phot routines.
3. Used daofind to detect stars in the image, and produce as a .coo file the list of their pixel coordinates.
4. Checked the resulting .coo file by superimposing the listed locations on the image, and looking for missed or false detections.
5. Repeated steps 2, 3, 4, changing parameters by trial and error to minimize missed or false detections, as will be discussed after this numbered list.
6. Used the phot routine to perform aperture photometry at the locations specified by the .coo file, producing a .mag file.
7. Used txdump to put the useful values in the .mag file (i.e. star IDs, coordinates, and magnitudes) into an easier-to-read .phot file.
As mentioned in step 5, I had to try adjusting parameters for daofind in order to not miss too many stars, or make too many false detections. At first, using the values listed in the table above, and leaving all unspecified values as their defaults (i.e. just pressing “enter” when the routine asks for a value), I noticed that many stars were left un-detected. So, I recalled one of the parameters, which I left as its default: the detection threshold, in sigmas. I tried to keep reducing it incrementally until almost all the stars were detected (because a lower threshold means progressively dimmer stars would pass it and thus be counted), and there were very few false detections. A higher threshold means fewer false detections, but more undetected stars, while a lower threshold means more false detections, but fewer undetected stars. A good compromise was a threshold of 2.5 sigmas (the default is 4).
After performing all 7 steps, I repeated step 4 – but superimposing the existing .coo file from obj720.fits onto the other image, obj724.fits. I saw that the positions still aligned nicely with the stars in the image, so I figured that the .coo file is still valid and I’d save some time by reusing it for steps 6 and 7 for obj725.fits.